EXERCISE 3

Simple Measurements

The Power increases on boot-up to around 5.8 W before settling back down to fluctuating between about 4.8 to 5.1 W. This fluctuation may be due to the changes in requirements of the pi over time, with the packet sending and receiving process potentially drawing more power.

Network Activity

1. Tcpdump shows the pi’s activity on the link to the PC. Through counting the number of packets that occur in 60 seconds, the events per second can be statistically approximated as around 27 events/min.

2. While the pi is pinging the PC continuously, the power draw increases from around 4.8 W to about 5.3W.

When the PC is pinging the pi, the increase is up to around 5.1W.

It therefore seems to be more energy-expensive to send a packet than to receive, likely because it is an active process requiring the message to be created and sent to the the PC along with a timer, rather than just ‘reflecting’ back a ping from the PC.

3. When the client (PC) first started measuring packet transmission, the wattage increased to 5.8 W until the process was over, at which point it returned to around 4.8 W.

Initial rx-usecs: 57

With rx-usecs set to zero, the power drawn seemed to largely mirror that of the previous test with no significant changes. I had expected an increase in power consumption due to a sped up process drawing more energy in the same amount of time, but it’s likely this increase wasn’t high enough to be noticeable.

CPU Activity

When the stress-ng command was sent, the pi’s power consumption fluctuated between 6.3 – 7 W, much higher than the 5.8 W value from the iperf test.

Theoretical Experiments

1. Energy used by pi = 11.11 Wh = 1.111 x 10-2 kWh

New York Carbon Impact = 0.261 kgCO2/kWh

Carbon Footprint = 1.111 x 10-2 x 0.261 = 2.90 x 10-3 kgCO2 = 2.9 gCO2

2. Total Carbon Footprint = 30 x 109 x 2.90 x 10-3 = 87 000 000 kgCO2

This is a somewhat insignificant number considering the yearly worldwide rate is inn the order of magnitude of 1012. This is unlikely to be an accurate measure, as a raspberry pi is relatively small and probably doesn’t use as much power as the average device.